# Setup Tasks for Homework #2
Using the command lines below, create the required folder tree for homework #2 in your HOME directory.

$ mkdir -p ~/ece3220/hw/02/{p1,p2,p3,p4}

Store a copy of the homework handout file ece3220-hw02-handout.odt into your folder ~/ece3220/hw/02/. A download link for the homework handout file is provided on Canvas on the assignment page for this homework assignment. Use the word processing program LibreOffice Writer to open and edit this file.

$ cd ~/ece3220/hw/02/
$ ls
ece3220-hw02-handout.odt p1 p2 p3 p4
$ libreoffice --writer ece3220-hw02-handout.odt &
# Problem #1. C++ Name Mangling

Using the command line below, make folder p1 your current working directory.

$ cd ~/ece3220/hw/02/p1/

Using the command lines below, create a C source code file demo-c.c and a symbolic link file named demo-cc.cc that “points to” the file demo-c.c. Note that the file names demo-c.c and demo-cc.cc refer to the same file; consequently, any changes made in file demo-c.c also appear in file demo-cc.cc and vice versa.

$ echo "void foo() { }" > demo-c.c
$ ln -s demo-c.c demo-cc.cc

Create a Makefile whose contents are as shown in Listing 1. The .PHONY rule all uses make’s built-in rules to create/update the prerequisite files specified by the variable $(OBJS)—i.e., the object files demo-c.o and demo-cc.o—from the C/C++ source code files demo-c.c and demo-cc.cc, respectively. After make creates/updates the prerequisite files for the .PHONY target all, make then invokes the rule’s the recipe line nm $(OBJS) which uses program nm to display the symbol table within each object file.

CSOURCES := $(wildcard *.c) / CFLAGS := -std=c11 / COBJS := $(CSOURCES:.c=.o) / CXXSOURCES := $(wildcard *.cc) / CXXFLAGS := -std=c++11 / CXXOBJS := $(CXXSOURCES:.cc=.o) / OBJS := $(COBJS) $(CXXOBJS) / .PHONY : all / all : $(OBJS) / nm $(OBJS) / .PHONY : clean / clean : ; rm -f $(OBJS)

Listing 1: Makefile source code for problem 1.

Invoke make to create the object files demo-c.o and demo-cc.o and display each object file’s symbol table (see Figure 1).

$ make / cc -std=c11 -c -o demo-c.o demo-c.c / g++ -std=c++11 -c -o demo-cc.o demo-cc.cc / nm demo-c.o demo-cc.o / demo-c.o: / 0000000000000000 T foo / demo-cc.o: / 0000000000000000 T _Z3foov

Figure 1.

Note that in object file demo-c.o (created from the C translation unit) the symbol for function foo is foo, while in object file demo-cc.o (created from the C++ translation unit) the symbol for function foo is _Z3foov.

In Table 1 under the column heading “demo-c.o”, for the “Function Syntax” void foo() {}, I’ve recorded the symbol for function foo as shown in demo-c.o’s symbol table (‘foo’).

In Table 1 under the column heading “demo-cc.o”, for the “Function Syntax” void foo() {}, I’ve recorded the symbol for function foo as shown in demo-cc.o’s symbol table (‘_Z3foov’).

Question P1.1. (6 points) For the remaining “Function Syntax” values in Table 1 for function foo, store the function syntax value in file demo-c.c and then re-run make; see the Hint below. Using steps 6 and 7 as your guide, fill in the remaining cells in Table 1 for each function syntax.
(n.b. Recall that demo‑cc.cc is linked to file demo-c.c; any changes you make to demo-c.c are also made to demo‑cc.cc.)

# Hint
$ echo "int foo(const char *p) { return 0; }" > demo-c.c
$ make

Table 1: Your answers for question P1.1.
Function Syntax	demo-c.o	demo-cc.o
void foo() {}	foo	_Z3foov
int foo(const char *p) { return 0; }
const char * foo(int I) { return 0; }
float foo(double d) { return 5.0F; }

Question P1.2. (5 points) Is function foo’s return type identified by any of the symbol table symbols in Table 1 under the column headings “demo-c.o” and “demo-cc.o”?

WRITE YOUR ANSWER HERE...
1. Question P1.3. (5 points) In C++, does a function’s signature include the function’s return type? (Hint: Research the topic “function signature” for the C++ programming language.)

WRITE YOUR ANSWER HERE...
# Problem 2. Function Overloading
Using the command line below, make folder p2 your current working directory.

$ cd ~/ece3220/hw/02/p2/

Copy the Makefile from problem 1 into folder p2. (See also Listing 1.)

$ cp ../p1/Makefile .

Create a C++ source code file named demo-cc.cc whose contents are as shown in Listing 2. Notice that this C++ source code file has four functions named `foo’ whose function signatures are all different. This is referred to as “function overloading”.
void foo() { } / int foo(const char *p) { return 0; } / const char * foo(int I) { return 0; } / float foo(double d) { return 5.0F; }

Listing 2: C++ source code for file demo-cc.cc for Problem 2.

Invoke make to create the object file demo-cc.o and display its symbol table.

$ make

Create a C source code file named demo-c.c whose contents are exactly the same as the C++ source code file demo-cc.cc

$ cp demo-cc.cc demo-c.c

Invoke make to create the object file demo-c.o and display its symbol table. (Hint: This step will fail!)

$ make
cc -std=c11 -c -o demo-c.o demo-c.c
demo-c.c:2:5: error: conflicting types for 'foo'
 int foo(const char *p) { return 0; }
     ^
(etc...)

Question 2.1. (5 points) The contents of files demo-cc.cc and demo-c.c are identical. Why does the C compiler gcc emit the error message “demo-c.c:2:5: error: conflicting types for 'foo'” when it translates the C source code in file demo-c.c? Note that the C++ compiler g++ does not emit any error/waring messages as it successfully translates the C++ source code in file demo‑cc.cc into the object file demo-cc.o. (Hint: Look at the symbols for function foo in Table 1 for object files demo-c.o and demo-cc.o.)

WRITE YOUR ANSWER HERE...
# Problem 3. Calling Functions in a C Translation Unit from a C++ Translation Unit
## References
[1]	Language Linkage (cppreference.com)
https://en.cppreference.com/w/cpp/language/language_linkage
[2]	Language Linkage (C++ Only) (IBM.com)
https://www.ibm.com/support/knowledgecenter/en/SSLTBW_2.3.0/com.ibm.zos.v2r3.cbclx01/cplr020.htm

Using the command line below, make folder p3 your current working directory.

$ cd ~/ece3220/hw/02/p3/

Create a Makefile whose contents are as shown in Listing 3.

PROGRAM := demo / CSOURCES := $(wildcard *.c) / CFLAGS := -std=c11 / COBJS := $(CSOURCES:.c=.o) / CXXSOURCES := $(wildcard *.cc) / CXXFLAGS := -std=c++11 / CXXOBJS := $(CXXSOURCES:.cc=.o) / OBJS := $(COBJS) $(CXXOBJS) / .PHONY : all / all : $(PROGRAM) / # Note that I am using the C++ compiler $(CXX) to perform the linking step! / $(PROGRAM) : $(OBJS) / $(CXX) $(LDFLAGS) -o $@ $^ $(LOADLIBES) $(LDLIBS) / .PHONY : clean / clean : ; rm -f $(PROGRAM) $(OBJS)

Listing 3: Makefile source code for problem 3.

Create a C++ source code file named demo-cc.cc whose contents are as shown in Listing 4.

/* demo-cc.cc */ / int main() / { / foo(); // defined in the C source file demo-c.c / return 0; / }

Listing 4: C++ source code for file demo-cc.cc for Problem 3.

Create a C source code file named demo-c.c whose contents are as shown in Listing 5.

/* demo-c.c */ / #include <stdio.h> / void foo() / { / printf("Hello, World!\n"); / }

Listing 5: C source code for file demo-c.c for Problem 3.

Invoke make to build the executable file demo. (Hint: This step will fail!)

Question 3.1. (10 points) Make the necessary changes to the C++ source code in file demo‑cc.cc so that you can successfully build and execute the program file demo. Your solution must not modify the C source code in file demo-c.c, and function main() in C++ source file demo‑cc.cc must directly invoke function foo() located in the C source code file demo-c.c.
# Problem 4. Calling Functions in a C++ Translation Unit from a C Translation Unit
See also the “References” section from Problem 3.

Using the command line below, make folder p4 your current working directory.

$ cd ~/ece3220/hw/02/p4/

Copy the Makefile from problem 3 into folder p4. (See also Listing 1.)

$ cp ../p3/Makefile .

Create a C source code file named demo-c.c whose contents are as shown in Listing 6.

/* demo-c.c */ / int main() / { / foo(); // defined in the C++ source file demo-cc.cc / return 0; / }

Listing 6: C source code for file demo-c.c for Problem 4.

Create a C++ source code file named demo-cc.cc whose contents are as shown in Listing 7.

/* demo-cc.cc */ / #include <iostream> / void foo() / { / std::cout << "Hello, World!" << std::endl; / }

Listing 7: C++ source code for file demo-cc.cc for Problem 4.

1. Invoke make to build the executable file demo. (Hint: This step will fail!)
2. Question 4.1. (10 points) Make the necessary changes to the source code in files demo‑c.c and demo‑cc.cc so that you can successfully build and execute the program file demo. Your solution must not modify function main() in file demo-c.c nor function foo() in file demo‑cc.cc, and function main() in file demo-c.c must invoke function foo() in file demo-cc.cc.
# Homework Deliverable
Using the command line below, make folder ~/ece3220/hw/02/ your current working directory.
$ cd ~/ece3220/hw/02/

Ensure this handout file (ece3220-hw02-handout.odt) with your written answers inside it is stored in the folder ~/ece3220/hw/02/.

$ ls
ece3220-hw02-handout.odt Makefile p1 p2 p3 p4

Create a Makefile whose contents are exactly as shown in Listing 8.

COURSE := ece3220 / CATEGORY := hw / ASSIGNMENT_ID := 02 / ASSIGNMENT := $(COURSE)-$(CATEGORY)$(ASSIGNMENT_ID) / USER_MODULE := $(ASSIGNMENT)-$(USER) / DELIVERABLE := $(USER_MODULE).tar.gz / HANDOUT := $(ASSIGNMENT)-handout.odt / CWD := $(notdir $(PWD)) / SUBDIRS := $(shell find . -mindepth 1 -type d) / .PHONY : dist / dist : $(DELIVERABLE) / $(DELIVERABLE) : check clean / tar -czf ../$@ -C .. $(CWD) --transform="s:^$(CWD):$(USER_MODULE):" \ / --exclude=.*.swp --exclude=.~lock.*.odt\# / mv ../$@ . / .PHONY : check / check : / @if ! [ -f $(HANDOUT) ]; then \ / >&2 echo "Required file '$(HANDOUT)' is missing. Aborting..."; \ / exit 1; \ / fi / .PHONY : clean / clean : / -rm -f $(DELIVERABLE) / @for m in $(SUBDIRS); do \ / if [ -d "$$m" ] && [ -f "$$m/Makefile" ]; then \ / $(MAKE) -s -k -C $$m $@; \ / fi; \ / done

Listing 8: Makefile source code for problem 3.

Invoke make to build the deliverable tarball file ece3220-hw02-${USER}.tar.gz where $⁠{USER} is your username (i.e., your pawprint).
$ make
rm -f ece3220-hw02-${USER}.tar.gz
tar -czf ../ece3220-hw02-${USER}.tar.gz -C .. 02 \
        --transform="s:^02:ece3220-hw02-${USER}:" \
        --exclude=.*.swp \
        --exclude=.~lock.*.odt\#
mv ../ece3220-hw02-${USER}.tar.gz .

$ ls
ece3220-hw02-${USER}.tar.gz ece3220-hw02-handout.odt Makefile p1 p2 p3 p4

$ tar tf ece3220-hw02-${USER}.tar.gz
ece3220-hw02-${USER}/
ece3220-hw02-${USER}/p1/
ece3220-hw02-${USER}/p1/demo-c.c
ece3220-hw02-${USER}/p1/demo-cc.cc
ece3220-hw02-${USER}/p1/Makefile
ece3220-hw02-${USER}/p2/
ece3220-hw02-${USER}/p2/demo-cc.cc
ece3220-hw02-${USER}/p2/demo-c.c
ece3220-hw02-${USER}/p2/Makefile
ece3220-hw02-${USER}/p3/
ece3220-hw02-${USER}/p3/Makefile
ece3220-hw02-${USER}/p3/demo-c.c
ece3220-hw02-${USER}/p3/demo-cc.cc
ece3220-hw02-${USER}/p4/
ece3220-hw02-${USER}/p4/Makefile
ece3220-hw02-${USER}/p4/demo-c.c
ece3220-hw02-${USER}/p4/demo-cc.cc
ece3220-hw02-${USER}/ece3220-hw02-handout.odt
ece3220-hw02-${USER}/Makefile

$ tree
.
|-- ece3220-hw02-${USER}.tar.gz # <- Upload this file only
|-- ece3220-hw02-handout.odt
|-- Makefile
|-- p1
| |-- demo-c.c
| |-- demo-cc.cc -> demo-c.c
| `-- Makefile
|-- p2
| |-- demo-c.c
| |-- demo-cc.cc
| `-- Makefile
|-- p3
| |-- demo-c.c
| |-- demo-cc.cc
| `-- Makefile
`-- p4
    |-- demo-c.c
    |-- demo-cc.cc
    `-- Makefile

4 directories, 15 files

Using the SUBMIT ASSIGNMENT link provided with this assignment on Canvas, upload a copy of your tarball file ece3220-hw02-${USER}.tar.gz for grading.

Done!